## Slide 1: FOSSEE Semester Long Internship
Nikhil Sharma
Malaviya National institute of technology Jaipur
Guided by:
Professor Janani Srree Muralidharan

## Slide 2: Case Study 1: CFD Simulation of flow through pipe: A comparative study on cyclic and inlet-outlet type boundary conditions in OpenFOAM
Solver utilized: pimpleFoam

## Slide 3: Introduction
Periodic/cyclic boundary conditions are very commonly utilized in industrial CFD applications.
Two coupled boundary patches are treated as if they are physically connected.
Figure: Different types of cyclic boundary conditions
Notes: Flux across the coupled patches is same in magnitude but opposite in sign.

## Slide 4: Modifying the governing equation for using periodic boundaries
  Need for modifying the governing equation:
  As the coupled patches are considered to be physically connected, there exists no potential difference/pressure gradient for driving the flow.
  Pressure gradient is thus explicitly added to governing equation as a source term.
  To add this source term without modifying source code, fVOptions functionality of OpenFOAM is utilized. Single region momentum source namely meanVelocityForce is applied.

## Slide 5: Periodic behaviour exhibited by flow fields
  The fully developed flow profile repeats itself in successive of cross section that are separated from each other by a period length (L).
  Pressure field does not exhibit the same kind of periodic behaviour as velocity.
Figure: Fully developed flow profile

## Slide 6: Problem Statement
The problem statement can be defined as:
  To solve for a laminar pipe flow through a pipe using cyclic boundary conditions and compare the results with that of a full length pipe and analytical results obtained using the Hagen–Poiseuille equation.
  To solve for a turbulent flow (using standard k-epsilon model) through a pipe using cyclic boundary conditions and compare the results with that of a full length pipe.
  To solve for the same turbulent flow using different turbulence models (realizable k-epsilon, k-omega and k-omega SST) and compare the results with each other.

## Slide 7: Geometry, mesh and other parameters
Due to flow being axis-symmetric, only a sector is modelled as computational domain.
A structured mesh with first cell in the log law region has been prepared using blockMesh.
As the boundary condition, standard wall functions are employed.
Figure: View of the mesh used

## Slide 8: Result 1: Laminar flow through pipe
Table: Comparison of CFD and analytical results
Figure: Velocity profile for laminar flow

## Slide 9: Result 2: Turbulent flow through pipe
Pressure gradient:
  in full length pipe = 7162.634 Pa/m
  in fully developed region of full length pipe = 6958.244 Pa/m
  in cyclic pipe = 6945.924 Pa/m
Figure: Velocity profile for turbulent flow

## Slide 10: Result: Turbulent flow through pipe
Table: Average value of parameters at cross sections in full length pipe
Table: Errors in pressure gradient calculation

## Slide 11: Conclusions
By simulating flow through periodic pipe it is seen that cyclic boundaries can accurately predict the flow profiles and significantly reduce the computational effort as it is difficult to capture fine details around the boundary layer and describe the gross motion at the same time.
Also it was found that the pressure gradient values obtained using cyclic and full length pipe slightly differ from each other and the difference is well within acceptable limits.

## Slide 12: Case Study 2: CFD analysis of flow past staggered tube array using 2D RANS turbulence models
Solver utilized: pimpleFoam

## Slide 13: Introduction
A tube bank consists of a of tube bundle bathed in a fluid, generally utilized to either cool or heat the material flowing through the tube.
Basic tube bank patterns are as shown.
Figure: Different Tube bank patterns

## Slide 14: Details of the experiment
Experimental studies on an iso-thermal flow through the staggered tube bank shown were performed by Simonin and Barcouda(1988).
Experimental database of the work was released by the European Research Community on Flow Turbulence and Combustion in 1993.
Figure: Experimental domain

## Slide 15: Problem Statement
In the experimental results, flow is observed to develop periodically repeating flow profiles after flowing past initial tube rows.
The objective is to simulate flow past staggered the same tube bank array using different 2D RANS model with periodic boundaries in both stream-wise and transverse directions.
Figure: Computational domain used by Kulasekharan and Prasad

## Slide 16: Geometry and mesh
Figure: Geometry of unit cell
Figure: Mesh

## Slide 17: Result : Velocity contour
Figure: Velocity contour showing periodic behaviour

## Slide 18: Result :Plot of Non-dimensional velocity
Figure: Plot of non-dimensional velocity extracted along line 1
Stream-wise velocity
Transverse Velocity

## Slide 19: Result : Plot of Non-dimensional velocity
Stream-wise velocity
Transverse Velocity
Figure: Plot of non-dimensional velocity extracted along line 2

## Slide 20: Comparing the results
Table: Percentage error in the non dimensional velocity

## Slide 21: Conclusions
By doing the simulations it can be concluded that 2D RANS models used in our case are not suitable for satisfactorily predicting the flow features.
Kulasekharan and Prasad have also arrived at similar conclusion. They performed simulations using nine different 2D RANS models and found none of these models to be suitable for accurately predicting the flow features.
Therefore a DNS or LES simulation may be attempted.

## Slide 22: Thank You