## Slide 1
SCILAB CASE STUDIES
AASHWIN VAIDYA
B.E, ELECTRONICS & TELECOMMUNICATION IET DAVV, INDORE, MADHYA PRADESH
GUIDE : PROF. PRABHU RAMACHANDRAN IIT BOMBAY | MENTOR : RASHMI PATANKAR
JULY 2026
FOSSEE SUMMER FELLOWSHIP REPORT

## Slide 2
Music Genre Classifier Using Feed Forward Neural Network
Single-Digit DTMF Generator and Detector
using Goertzel Algorithm
ECG Signal Processing and Heart Rate Frequency Detection
Case Studies Overview
Extracted features of 10,000 3 second audio files
Feed Forward Neural Network with Adam Optimization
Neural Convergence Curve and Heat Map to validate model
Sine waves and pulse signal for DTMF generation
8 Goertzel Detectors for effective frequency detection
Verification tests
ECG Signal uploading in .csv format
ECG Filtering to remove noise
R-Peaks filtering to estimate heart rate

## Slide 3
Case Study 1: Music Genre Classifier using Feed Forward Neural Network
The Challenge:
Solution:
Unlike images, audio files are unstructured signals that cannot be directly fed into neural network
Training the network with mel spectrograms requires significant processing
Very slow training time
Replace heavy 2D Mel-Spectrogram image matrices low-dimensional statistical matrices
Uses feed forward neural network instead of convolutional neural network Significantly dropping the workload
Implement feature scaling and optimize hidden layer dimensions to enforce model generalization

## Slide 4
Extracted 57 features from 10,000 audio files for training the model
Normalized and encoded the data to make it ready for training
Shuffled the dataset
Initialized a neural network with two hidden layers
ReLu and Softmax Activation Functions
Adam Optimization for updating weights and biases
Key Features
Flowchart

## Slide 5
Neural Convergence Curve
Fig. 02
Results
Fig.01
Cross-Entropy Loss for every 50 epoches and training accuracy

## Slide 6
Results
Fig.03
Heat Map of Confusion Matrix

## Slide 7
Result Comparison with Reference Paper

## Slide 8
Case Study 2: Single-Digit DTMF Generator and Detector using Goertzel Algorithm
Objectives:
Generate a combination of two frequencies to represent a digit
Optimize Targeted Frequency Detection for Low Latency
Successfully decode the digit from the DTMF signal
Generates a Single DTMF Signal at a time
Utilizes bank of parallel digital Infinite Impulse Response (IIR) filters
Implements the Goertzel algorithm for discrete frequency detection
Rejects out of band speech signals
Validates the received signal using verification tests
Key Features:

## Slide 9
Xcos Diagram

## Slide 10
DTMF Signal for Digit ‘7’
Fig. 02
Results
Fig.01
Fig.03
Energy Output for Digit ‘7’
Validation Tests, Low Frequency, High Frequency and Successful Detection of Digit ‘7’

## Slide 11
Result Comparison with Reference Paper

## Slide 12
Case Study 3: ECG Signal Processing and Heart Rate Frequency Detection
Objectives:
Design a Biomedical Signal Processing Pipeline for analyzing ECG signals
Implement a Digital Filter Cascade for Noise Removal
Isolate and Detect Morphological Features
Compute Real-Time Diagnostics like Heart Beat
Uses a biquad notch filter configured to eliminate 50 Hz power
Uses a low-pass moving-average smoothing filter to remove low-frequency baseline wander caused muscle movement
QRS Complex Segmentation by amplifying the sharp slope while suppressing P and T waves.
Computes R-R intervals to output heart rate in BPM
Key Features:

## Slide 13
GUI Implementation
The GUI displays the raw ECG graph, the filtered graph and R-peaks filtered graph together for comparison
Implemented slider to dynamically change the amount of 50Hz noise
numeric indicators displaying heart rate (BPM) and calculated R-R intervals.
A simple interface to easily load raw clinical ECG data files directly into the Scilab workspace.

## Slide 14
Result Comparison with Reference Paper

## Slide 15
THANK YOU